## Slide 1
With 10” backyard telescopes
Tom Mozdzen, Rick Scott, Phil Mauskopf
October 30, 2024
Intensity Interferometry
Arizona State University

## Slide 2: Background
Work at ASU on intensity interferometry started in 2012
Technology did not exist at the time
  Developed CASPER ROACH-based time tagger
  Started testing single photon counting detectors on telescopes
  Tried Kitt Peak 90 inch – measured counts
Paper by G. Pilyavsky, 2017
Goal: Low cost, scalable interferometer with small telescopes
Status: Measured correlations with 10 inch telescopes from Sirius
  SNR = 7 in 13.5 hours
Smallest aperture correlation measurement to date

## Slide 3: Equipment for an Intensity Interferometer
Backyard Telescopes
3.3 m Baseline
10 m Baseline
Notes: Telescopes in our backyard set up
  Telescopes
    10” f/4.6 home- made Lurie-Houghton telescope
    10” F/4 Meade Schmidt-Newtonian (SN10)
      The SN10 replaced a 10” f/6.3 Meade Schmidt-Cassegrain (with focal reducer)
  The Lurie-Houghton is in a 10’ rotating dome and is the reference scope
  The Schmidt-Newtonian is mounted on external piers depending on the baseline in use
    There are pier locations for 3.3 m, 10 m, and 24m baselines
The telescopes need to be guided over the course of the night to keep the star under study on the fiber optic cable to maintain a high count rate.

## Slide 4: Equipment for an Intensity Interferometer
Telescope Guiding Improvement
  Piggyback mounted guide scope and camera
    Long-term drift due to differential flexure
    Needed to reset centering every 20 to 30 minutes
    Orange on the plot is 1 hour of operation
  On-axis guider built into the JaZeye
    No long-term drift
    Can operate for hours with no recentering
    Blue on the plot is 3 hours of operation

## Slide 5: Equipment for an Intensity Interferometer
JaZeye Optical System

## Slide 6: Equipment for an Intensity Interferometer
JaZeye Narrowband Filter
  We measured the narrowband filters we're currently using on stars with an Agilent Cary 5000 spectrophotometer
  The filters have the following characteristics:
    Center wavelength = 589.25 nm
    Bandwidth = 1.2 nm
    Overlapping bandwidth = 1.1 nm
    tcoh = 0.78 ps

## Slide 7: Equipment for an Intensity Interferometer
Single Photon Detectors: SPADs
  Input is fed by a fiber optic cable to reduce loading on the JaZeye
  Our old SPADs had a timing jitter of 350 ps vs 32 ps for our new SPADs
Old SPAD
New SPAD

## Slide 8: Equipment for an Intensity Interferometer
Bench Set Up
Initial testing was performed on an optical bench in the lab
The bench setup simulates a star from two telescopes
  A beamsplitter is used to make a star for each JaZeye/detector system
  No motion to track
  No seeing effects

## Slide 9: Equipment for an Intensity Interferometer
Bench Set Up Block Diagram
  Components to the right of the beamsplitter is the same as on the telescopes

## Slide 10: System Efficiency
Component Efficiency | Lurie-Houghton Telescope (%) | Meade SN10 Telescope (%)
Telescope Optics | 71 | 72
Jazeye Optics | 74 | 74
Fiber Optic Cable | 92 | 92
Total Optics | 49 | 49
Detector @ 589 nm | 39 | 39
Total System | 19 | 19

## Slide 11: Typical Data – counts and timestamps
Sirius count rates are about 2 million photons per second
3 hrs of data ~ 40 billion stamps
4 bytes per event -> 160 GB
Count Rate 1
Count Rate 2
5 hrs
~20% of Photons detected

## Slide 12: Shift the correlation away from t = 0

## Slide 13: Our Favorite Equations
Integrate

## Slide 14: Coherence Signal

## Slide 15: Gaussian Fitting Results
Source | 2x Fit Area (ps) | Fit Height (10-3) | Sigma Fit (ps) | tres derived (ps) | ¦V12(3.3 m)¦2
Sirius | 0.74 +/- 0.26 | 1.1 +/- 0.2 | 138 +/- 26 | 346 +/- 65 | 0.95 +/-0.33
With:
Tcoh = 0.78 ps from the filter shape
SNR ~ 7.0
Expected |V12(3.3 m)|2 = 0.94 +/-0.01

## Slide 16: Bonus Equations

## Slide 17: IV. Future Plans
Collection time reduction
  More baselines simultaneously
  Multiple Telescopes
  Spectrometers – use multiple wavelengths to reduce collection time
  Use both polarizations
  Slightly larger telescope
    12" to 14" would still be low cost
  Lower system jitter – 6x
    2.4x less collection time
Measure exotic objects
  Quasars
    Accretion discs around black holes

## Slide 18: Questions?

## Slide 19: Backup Material

## Slide 20: Data Collection Sessions
Date (2024) | Start Time (MST) | Mins before Transit | Time on Sky (h) | Channel 1 Rate (Mcps) | Channel 2 Rate (Mcps) | Temp Begin to End (C)
Jan 30 | 21:13 | 84.2 | 4.25 | 1.9 | 2.0 | 16 --> 11
Feb 13 | 20:34 | 68.2 | 4.88 | 1.7 | 1.9 | 14 --> 7
Feb 14 | 20:30 | 68.3 | 4.41 | 1.8 | 2.0 | 14 --> 7
Totals |  |  | 13.55 | 1.8 | 2.0 | 

## Slide 21: Binning Statistics
Statistic | 25 ps | 50 ps | 100 ps | 200 ps
Mean (107) | 0.443 | 0.887 | 1.77 | 3.55
sSTD (103) | 2.13 | 3.02 | 4.18 | 5.76
sPoisson (103) | 2.10 | 2.97 | 4.20 | 5.94
Peak/sPoisson | 3.60 | 3.92 | 4.94 | 6.26
Fit tres (ps) | 326 | 346 | 346 | 363
SNRcalc | 7.2 | 7.0 | 7.0 | 6.9

## Slide 22: Gaussian Fitting Results
Source | tcoh 2x Fit Area (ps) | Fit Height (10-3) | Sigma Fit (ps) | tres derived (ps)
Siriusa | 0.74 +/- 26 | 1.1 +/- 0.2 | 138 +/- 26 | 346 +/- 65
Hab | 11.8 +/- 0.9 | 32 +/- 1 | 75 +/- 3 | 188 +/- 8
Hac | 8.6 +/- 0.9 | 52 +/- 2 | 33 +/- 1 | 82 +/- 4
Had | 10.8 +/- 0.9 | 58 +/- 3 | 26 +/- 2 | 65 +/- 4
a |V12(3.3m)|2 = 0.94 +/- 0.01 for Sirius and 1.00 for Ha
b Time Tagger sjitter = 42 ps, Gaussian Fit
c Time Tagger sjitter = 8 ps, Gaussian Fit
d Time Tagger sjitter = 8 ps, Lorentzian Fit

## Slide 23: Optical Path Delay vs Hour Angle

## Slide 24: Sirius Baseline Variations vs Hour Angle

## Slide 25: Signal Build up
After 1 hr
After first night (4 ¼ h)
After two days (9 h)
After three days (13 ½ h)

## Slide 26
Sirius
Cumulative Results – hour by hour

## Slide 30: Three Nights – various bin sizes
25 ps bins
50 ps bins
100 ps bins
200 ps bins
250 ps bins
500 ps bins
1000 ps bins